## Slide 1
Supervisor:
S.M Tanbinul Hoque
Lecturer, Department of EEE
Leading University, Sylhet
Co-Supervisor:
Mirza Md. Mahbubur Rahman
Lecturer, Department of EEE
Leading University, Sylhet
"An IoT-Based Home Automation System with Security and Remote Monitoring Using NodeMCU and ESP32-CAM"
LEADING UNIVERSITY , SYLHET
Electrical & Electronic Engineering

## Slide 2
Authors
Md Rahatul Islam
1912070052
Md. Jillur Rahman
2132079003
Shopon Kanto Das
2132079007
Leading University
02
Electrical & Electronic Engineering

## Slide 3
Table of Contents:
Introduction
Components
Software
Objectives
Literature review
Methodology Flowchart
Design Layout
Implementations
Cost Estimation
Future Scope
Limitations
Conclusion
References
Leading University
03
Electrical & Electronic Engineering

## Slide 4
Introduction
This IoT-based Home Automation System provides efficient control and monitoring of household appliances such as lights, fans, and a water pump, using NodeMCU as the central controller. The system integrates key features like seismic detection for automatic appliance shutdown during earthquakes, gas leakage alerts, water level monitoring with automatic pump control, and an anti-theft system linked to the ESP32-CAM for real-time image capture.
All devices are controlled remotely via the Blynk app, offering both remote management and real-time alerts for enhanced safety and convenience.
Leading University
04
Electrical & Electronic Engineering

## Slide 5
How does it work?
The NodeMCU controls appliances based on sensor inputs and commands from the Blynk app. The water pump operates automatically using the XKC-Y26-V water level sensor, turning off when the tank is full. For security, two PIR motion sensors are used to cover a wider area for anti-theft detection. When motion is detected, the ESP32-CAM captures images and sends them to the Blynk app. The MQ-5 gas sensor detects gas leaks, activating a buzzer and sending real-time alerts via the Blynk app. In the event of seismic activity, the ADXL345 accelerometer detects vibrations and triggers an automatic shutdown of all connected appliances through relays, ensuring household safety.
Leading University
05
Electrical & Electronic Engineering

## Slide 6
Service 2
The ESP8266 NodeMCU is a versatile microcontroller unit that acts as the main controller in this project. Equipped with built-in Wi-Fi capabilities, it allows seamless integration with IoT platforms like Blynk for remote control and monitoring.
Features:
Operating Voltage: 3.3V
Power Supply via Micro USB Port: 5V
Working temperature: -40°C ~ +125°C
Flash size: 4MB
Transfer rate: 110-460800bps
ESP8266 NodeMCU
Figure 01: ESP8266 NodeMCU V3
Components
Leading University
06
Electrical & Electronic Engineering

## Slide 7
Service 2
This sensor is integrated into this home automation system to detect hazardous gases like LPG, natural gas, or coal gas, ensuring safety in real-time.
Features:
Operating Voltage: 5V
Gas Detection Range: 200–10,000 ppm (LPG, methane, natural gas)
Sensitivity: High sensitivity to LPG, natural gas, and coal gas
Output Type:
Analog Output: Proportional to gas concentration
Digital Output: Triggered when gas levels exceed a threshold
Preheat Time: ~20 seconds for stabilization
MQ-5 Gas Detector Sensor
Figure 02: MQ-5 Gas Detector Sensor
Components
Leading University
07
Electrical & Electronic Engineering

## Slide 8
Service 2
This non-contact liquid level sensor is applicable to non-metallic containers without direct contact with the liquid. This sensor plays a critical role in our system by automating the water pump, turning it off when the tank reaches a predefined water level.
Features:
Operating Voltage: 5V
Output Signal: Digital output (HIGH or LOW)
Sensing Range: Supports tank wall thickness up to 13mm
Response Time: Fast detection within 500ms
Water Level Sensor
Figure 03 : Contactless Water Level Sensor (XKC-Y26-V)
Components
Leading University
08
Electrical & Electronic Engineering

## Slide 9
Service 2
This key component, providing motion detection for security purposes. It uses infrared technology to detect the movement of objects (typically human beings) within its detection range.
Features:
Operating Voltage: 5V
Detection Range: 3–7 meters(can be adjusted)
Detection Angle:<140
Output: Digital(HIGH/LOW)
Motion Sensor
Figure 04 : HC-SR501 PIR Motion Sensor
Components
Leading University
09
Electrical & Electronic Engineering

## Slide 10
ADXL345 Triple-Axis Accelerometer:
Figure 05 : ADXL345
The ADXL345 operates by measuring the change in capacitance caused by the movement of a micro-machined structure inside the sensor. When the device experiences acceleration or vibrations (like seismic activity), the internal structure shifts, altering the capacitance and producing corresponding changes in the output signal.
Sensing Acceleration: The sensor detects acceleration across the X, Y, and Z axes by monitoring the displacement of its internal structure.
Digital Output via I2C/SPI: The detected acceleration data is converted into digital signals and transmitted via I2C(Inter-Integrated Circuit) or SPI(Serial Peripheral Interface) to the NodeMCU.
Seismic Detection Mechanism: The NodeMCU constantly reads the accelerometer data.
When the measured acceleration exceeds a predefined threshold (indicating seismic activity),
the NodeMCU triggers the relay module to shut off all connected appliances for safety.
Features
Operating Voltage: 3.3V Output: Digital (I2C/SPI Communication)
Measurement Range: ±2g, ±4g, ±8g, ±16g Sensitivity: Adjustable threshold for seismic event detection
Components
Leading University
10
Electrical & Electronic Engineering

## Slide 11
Service 2
The 4-channel 5V relay module controls 5V appliances like lights, fans, and a water pump in the prototype system. The relays receive low-voltage signals from the NodeMCU to switch these appliances on or off, providing flexible and safe control.
Features:
Operating Voltage: 5V DC
Switching Capacity: Supports appliances up to 250V AC / 10A, but used here for 5V
Appliances Control: Triggered by NodeMCU GPIO digital signals
Isolation: Provides electrical isolation between control signals and appliances for safe operation
Indicator LEDs: Show the ON/OFF status of each relay.
Relay
Figure 06: 5v Relay
Components
Leading University
11
Electrical & Electronic Engineering

## Slide 12
ESP32-CAM
The ESP32-CAM is a compact microcontroller module with a built-in camera designed for image capture and video streaming. In this project, the ESP32-CAM is dedicated to the anti-theft system, capturing images when motion is detected and sending them to the Blynk app for real-time monitoring. When the PIR motion sensors detect movement, they send a signal to the NodeMCU, which triggers the ESP32-CAM to capture an image. The captured image is then transmitted over Wi-Fi to the Blynk app, providing instant visual feedback for security monitoring
Features:
Microcontroller: ESP32 with integrated Wi-Fi and Bluetooth Camera
Resolution: 2MP, supports resolutions up to 1600x1200
Storage: Supports microSD cards for local image storage
Power Supply: 5V
Figure 07: ESP32-CAM
Components
Leading University
12
Electrical & Electronic Engineering

## Slide 13
Blynk Blynk app as the primary software platform for remote control and real-time monitoring of household appliances and security systems. The app connects to the NodeMCU and ESP32-CAM via Wi-Fi.
Key Functions:
Appliance Control: Turn lights, fans, and the water pump on/off remotely.
Real-Time Alerts: Notifications for gas leaks and seismic activity.
Water Monitoring: control the water pump.
Anti-Theft: ESP32-CAM captures and sends images when motion is detected.
Software Tools Used:
Blynk App: For control and alerts.
Arduino IDE: For programming NodeMCU and ESP32-CAM.
Blynk Library: Integrated into the Arduino code to establish communication between the hardware and the app.
Figure 08: Android App
Software
Leading University
13
Electrical & Electronic Engineering

## Slide 14
IoT- Based Control: Control lights, fans, and a water pump via the Blynk app with real-time monitoring.
Seismic Safety Shut down: Use the ADXL345 accelerometer to automatically shut off appliances during earthquakes.
Gas Leak Detection: Detect LPG (Liquefied Petroleum Gas), using the MQ-5 sensor, triggering a buzzer and sending app notifications.
Automatic Water Pump Control: Use the XKC-Y26-V sensor to automatically turn off the water pump when the tank is full.
Anti-Theft System: Detect motion with two PIR sensors and trigger the ESP32-CAM to send images to the Blynk app.
Energy Efficiency: Enable remote appliance control to reduce unnecessary energy use.
Objectives
Leading University
14
Electrical & Electronic Engineering

## Slide 15
Literature Review
1. An IoT-Based Home Automation System Using NodeMCU and Blynk IoT App(2022) This study developed a smart home system using NodeMCU and the Blynk IoT app, allowing users to control appliances remotely through a mobile interface [1]. But there is a lacking of security features like motion detection and camera integration for unauthorized access monitoring.
2. Gas Leak Detection, Monitoring, and Safety System Using IoT (2020) This system detects gas leaks using sensors, alerts users via a buzzer and cloud notifications, and controls gas flow with a solenoid valve [2]. But there is a lacking of integration with broader home automation features, such as connectivity with other smart security systems.
3. Arduino-Based Smart Security for Home Automation (2021) This research focused on home security automation using PIR motion sensors and a camera module to detect unauthorized entry [3]. But there is a lacking of real-time remote access and additional safety features like seismic or gas leak detection.
4. Theft Detection System Using PIR Sensor (2020) Implemented PIR motion sensors for intrusion detection and alert notifications [4]. But there is a lacking of a camera for evidence capture and real-time app monitoring.
5. Arduino-Based Home Automation Using IoT (2019) Developed a Wi-Fi-based home automation system that allowed users to control appliances remotely [5]. But there is a lacking of seismic safety shutdown and gas leakage detection, making it less secure for critical situations.
Leading University
15
Electrical & Electronic Engineering

## Slide 16
6. An IoT-Based Home Automation Using Android Application (2020) Used an Android app to control home appliances via Wi-Fi, enhancing user convenience [6]. But there is a lacking of motion-based security monitoring and automatic water pump control.
7. Arduino-Based Earthquake Detector Using Accelerometer (2018) Utilized an accelerometer (ADXL335) to detect earthquakes and trigger alerts [7]. But there is a lacking of integration with a home automation setup for appliance shutdown.
Contribution of This Project: This project improves upon traditional systems by using Wi-Fi for global control via the Blynk app. It automates appliance shutdown during earthquakes, integrates smart gas leak alerts with cloud notifications, and triggers immediate responses. Unlike manual water level monitoring, it automates pump control with a contactless sensor. It also enhances security by combining dual PIR sensors with ESP32-CAM for real-time image capture and app monitoring. Additionally, it optimizes energy use through remote appliance control.
Leading University
16
Electrical & Electronic Engineering
Literature Review

## Slide 17
Methodology Flowchart
Report Preparation
Troubleshoot Procedure, Carefully check all steps and setup
Implementations
System Design
Literature Review
Testing & Validation
tEND
tStart
Yes
NO
Leading University
17
Electrical & Electronic Engineering

## Slide 18
Figure 09: Block Diagram of the System
ESP-CAM
4-CHANNEL RELAY MODULE
Load 1 -Light
Load 2-Fan
BUZZER
Load 3-Water Pump
PIR SENSORS
ADXL345
Block Diagram of the System
Leading University
18
Electrical & Electronic Engineering
NodeMCU ESP8266
MQ-5
XKC-Y26-V
Blynk App

## Slide 19
Design Layout
Leading University
19
Electrical & Electronic Engineering

## Slide 20: Implementations (Cont.)
Leading University
Electrical & Electronic Engineering
20

## Slide 21: Implementations (Cont.)
Leading University
Electrical & Electronic Engineering
21

## Slide 22
Cost Estimation
SL | Accessories | Quantity | Cost (TK)
1 | DC Motor With Fan | 1 | 120
2 | NodeMCU ESP8266 | 1 | 450
3 | MQ-5 Gas Detector Sensor | 1 | 195
4 | Contactless Water Level Sensor (XKC-Y26-V) | 1 | 1150
5 | HC-SR501 PIR Motion Sensor | 2 | 186
6 | Active Speaker Buzzer Module | 1 | 49
7 | 5V 4 Channel Relay Module | 1 | 270
8 | Male to Female Jumper wires | 40 | 150
9 | Male to Male Jumper wires | 40 | 150
10 | Cable -USB A To Micro B | 1 | 200
11 | Submersible 3V Mini DC water Pump | 1 | 140
12 | LED | 1 | 20
13 | 5V 2A Power Adapter | 1 | 300
14 | ESP32-CAM With Mounting Accessories | 1 | 1495
15 | ADXL345 Triple-Axis Accelerometer | 1 | 468
16 | Others |  | 
 | Total |  | 
Leading University
23
Electrical & Electronic Engineering

## Slide 23
Future scope
Advanced Security Features: Integrate facial recognition and intrusion detection using the ESP32-CAM to enhance the anti-theft system with smarter, automated security responses.
Smart Energy Monitoring: Implement real-time energy tracking for individual appliances to help users monitor consumption, optimize usage, and reduce electricity costs.
Voice Assistant Integration: Enable control of appliances through voice commands by integrating with platforms like Google Assistant or Amazon Alexa for hands-free operation.
Geofencing Automation: Introduce location-based automation that can automatically turn appliances on or off when the user enters or leaves home.
Offline Functionality with Local Server: Add offline control capabilities using MQTT or a Raspberry Pi local server, allowing the system to function even without an internet connection.
Leading University
24
Electrical & Electronic Engineering

## Slide 24: Limitations
Electrical & Electronic Engineering
Leading University
25
False Triggers in Sensors:
PIR motion sensor may generate false alarms due to temperature changes, sunlight, or air flow &Accelerometer may detect vibrations from nearby activities instead of actual earthquakes.
Wi-Fi Dependency: System requires a stable internet connection for remote monitoring. Limited Detection Range: PIR sensor range is 3-7 meters, and water level sensor detects liquid only through non-metallic containers up to 20mm thick.

## Slide 25
Conclusion
System Design and Integration Completed: The home automation system, including seismic detection, gas leakage alerts, water level monitoring, and anti-theft features, has been fully integrated.
Component Implementation and Testing: All components have been successfully installed and the system has undergone thorough testing to ensure reliable operation.
Optimization Achieved: Debugging and adjustments were completed to ensure smooth performance, achieving the project’s goals of safety, efficiency, and remote control.
Leading University
26
Electrical & Electronic Engineering

## Slide 26
References
[1] T. Deenadayalan, J. J. Shirley, R. Prajapati, P. Singh, A. Biswas, and U. Soni, "An IoT-based Home Automation System using NodeMCU and Blynk IoT App," 2023 International Conference on System, Computation, Automation and Networking (ICSCAN), Pondicherry, India, 2023, pp. 1-7. [Online]. Available: https://ieeexplore.ieee.org/document/10394759/
[2] P. Kalpana, R. Vignesh, R. Sakthi Vignesh, and K. R. Saanjeev Kumar, "Gas Leak Detection, Monitoring, and Safety System Using IoT," International Journal of Recent Technology and Engineering (IJRTE), vol. 8, no. 6, March 2020. ISSN: 2277-3878 (Online). DOI: 10.35940/ijrte.F9041.038620. [Online]. Available: https://www.ijrte.org/
[3] T. Akilan, R. Srivastava, C. Chandraprabha, B. Ahmad, H. Islam, and M. Saif, "Arduino-Based Smart Security for Home Automation," 2021 3rd International Conference on Advances in Computing, Communication Control and Networking (ICACCCN), Greater Noida, India, 2021, pp. 804-809. ISBN: 978-1-6654-3811-7. [Online]. Available: https://ieeexplore.ieee.org/document/9725436.
[4] P. N. Saranu, G. Abirami, S. Sivakumar, M. RameshKumar, U. Arul, and J. Seetha, "Theft Detection System using PIR Sensor," 2018 4th International Conference on Electrical Energy Systems (ICEES), Chennai, India, 2018, pp. 656-660. ISBN: 978-1-5386-3695-4. [Online]. Available: https://ieeexplore.ieee.org/document/8443215.
[5] L. M. Satapathy, S. K. Bastia, and N. Mohanty, "Arduino Based Home Automation Using Internet of Things (IoT)," International Journal of Pure and Applied Mathematics, vol. 118, no. 17, pp. 769-778, 2018. [Online]. Available: http://www.ijpam.eu.
[6] P. S. N. Reddy, K. T. K. Reddy, P. A. K. Reddy, G. N. K. Ramaiah, and S. N. Kishor, "An IoT based Home Automation Using Android Application," in Proc. Int. Conf. Signal Process., Commun., Power Embedded Syst. (SCOPES), 2016, pp. 1-5. [Online]. Available: https://ieeexplore.ieee.org/document/9318084
[7] G. Naik S, A. R, A. D, A. M.D, and A. P, "Arduino Based Earthquake Detector using Accelerometer," International Journal of Advanced Research in Electrical, Electronics and Instrumentation Engineering, vol. 9, no. 7, pp. 2005-2008, July 2020. [Online]. Available: https://www.ijareeie.com/upload/2020/july/40_ARDUINO_NC.PDF
Leading University
27
Electrical & Electronic Engineering

## Slide 27
Thank you
Leading University
28
Electrical & Electronic Engineering

## Slide 28
Q & A
Leading University
29
Electrical & Electronic Engineering